## Slide 1: Automated Washing Machine using PIC16F877A
Name : Shalini Sharma
Intern at : Emertxe Information PVT.LTD

## Slide 2: C-PROGRAMMING
C program is used in System Software Development , Embedded Software Development , OS Kernel Development , Firmware , Middle-Ware & Driver Development.
C language is effectively used in various specific domains and it is a free-formatted language , Efficiency and portability.
Number System – Decimal , Octal , Hexadecimal , Binary.
Data representation – bit , byte , word.
Data types – Integral(char , int) , Floating point (float , double).

## Slide 3: Conditional Constructs :
Single iteration – if , if-else , if else if & switch case.
Multiple iteration – While , do while , for.
Unconditional – Continue , break.

## Slide 4: Learnt from Embedded C
Operators – Operates on its operands , Returns a value.
Array – Collection of data of same data type . In array Addresses are sequential.
Pointers – Parameter Passing mechanism in function , by passing the reference.
Functions – Pass by Value and Pass by reference (Return more than one value from a function) , Passing array , returning array & recursive.

## Slide 5: EMBEDDED SYSTEMS
Any combination of Hardware and Software which is intended to do a Specific task is called as Embedded System.
Categories – Stand-alone-Real time , Networked , Mobile.
Challenges in ES – Efficient Inputs/outputs , Embedding an OS , Code optimization , Testing and debugging.
REAL TIME ASPECTS :
Hard Real Time – It should meet its deadline Life Critical Application.
Firm Real Time – Similar to Hard Real Time.
Soft Real Time – It can have tolerance in meeting its deadline.

## Slide 6: Block Diagram of Washing Machine

## Slide 7: CLCD 8 bit and 4 bit mode.
            CLCD stands for character liquid crystal display.
It has two type of displays 16*2 and 16*4.
In our project we used 16*4 display.
It has total 16 interfacing lines.
D0 to D7 are data lines , it has build in controller it has its own ROM and RAM that controller can execute the instruction and data.
RS Line –register select line.
Rs value 1 - data
Rs value 0 – instruction.
Data processed by two methods-delay method and polling method.
In CLCD D0 to D7 are connected to port D & Rs and enable pin are connected to port E.
8 bit mode – D0 to D7.
4 bit mode D4 to D7.

## Slide 8: Tactile Key
A tactile switch allows electricity to flow in an electrical circuit by manually pressing the operating section. The switch is used to supply input signal to activate a device.
The switch activates when pressed and then turns off when released
There are many different types of tactile switches such as tactile pull up an pull down.

## Slide 9: TACTILE KEYPAD IN MATRIX KEY PAD.

## Slide 10: TIMERS
There are three types of timers in PIC16F877A microcontroller timer-0,timer-1 timer-2.
Timer can work as timer and controller like for counting internal pulses and external pulses.
Timer 0 is a 8 bit timer like it will count from 00 to ff then generate a interrupt.
There are various registers associated with timer 0 like TMR0 clock source select bit.
There are 15 interrupt sources in case of this microcontroller.
Timer 0 has a bit GIE if we set this bit it will enable all the interrupts.
GIE bit is common for all the function whether main.c or timer.c.

## Slide 11: Software Used
MPLAB X IDE –
MPLAB is a proprietary freeware integrated development environment for the development of embedded application on PIC & dsPIC controllers , and is developed by Microchip Technology.
PicSimLab simulator –
PicSimLab is a Realtime emulator of development boards with integrated MPLABX/avr-gdb debugger. PicSimLab supports some picsim microcontroller.

## Slide 12: PicSimLab Architecture

## Slide 13: IMPLEMENTATION

## Slide 14: IMPLEMENTATION
STEP 1 :
To turn on the washing machine user have to press Key 5 i.e. RB4

## Slide 15
Step 2 :
Power on screen with 3s delay.

## Slide 16
Step 3 :
Washing programs shows the different types of cloths which user want to wash like
Daily ,Heavy, Delicates, whites, stain wash, Eco cotton ,Woollens ,Bedsheets ,Rinse + Dry ,Dry only ,Wash only & aqua store
To select one of these user have to Long press RB3

## Slide 17
Step 4 :
This screen indicates different levels of water flow in the machine
Like Auto, Low, medium, High & Max
To select one of these user have to Long press RB3

## Slide 18
Step 5 :
This step gets user acknowledgement to start or stop the process
RB4 – Start & RB5 – Stop

## Slide 19
Step 6 :
This screen shows the users choice of
cloth type and time in MM:SS format.

## Slide 20
Step 7 :
This screen shows the process like Wash , Rinse , Spin and Dry
Time, start and pause options.

## Slide 21
At the time of washing if user opens the door by pressing RB0 this above screen will pop.

## Slide 22
Step 8 :
After all the process done washing machine displays the following screen.